## Slide 1
UD 3.6 metodi cromatografici per analisi enologiche
Alcuni metodi HPLC e GC
Organic acid : ionic chromatography (Oeno 23/2004)
Method of determination of biogenic amines in wine by high-performance liquid chromatography with photodiode array detection
Sucrose by high-performance liquid chromatography
Measuring ochratoxine A in wine after going through an immunoaffinity column and HLPC with fluorescence detection (Oeno 16/2001 revised by Oeno 349-2011)
HPLC-Determination of nine major anthocyanins in red and rosé wine
Analysis of volatile compounds in wines by gas chromatography
Method of determination of phthalates by gas chromatography/mass spectrometry in wines (Oeno 477/2013 revised by Oeno 596/2019)

## Slide 2
Organic acids Method OIV-MA-AS313-04
Wine organic acids may be separated and simultaneously determined by high performance liquid chromatography (HPLC).
Principle of method
Wine organic acids may be separated using two stationary phases: octyl-bonded silica and ion exchange resin columns. The acids are detected by spectrophotometric absorbance in ultraviolet.
For the determination of malic and tartaric acids, it is advisable to use an octyl-bonded silica column and for citric and lactic acids, an ion exchange resin column. The determination of these acids is performed with reference to an external standard analyzed under similar conditions.

## Slide 3
2. Apparatus
2.1. Cellulose membrane filtration apparatus (diameter of pores: 0.45 μm)
2.2. Octadecyl-bonded silica fitted cartridges (e.g. Sep Pak - Waters Assoc.)
2.3. High Performance Liquid Chromatograph equipped with:
— a 10 μL loop injector,
— a temperature control apparatus,
— spectrophotometer detector capable of making absorbance measurements at 210 nm,
— a chart recorder, or integrator.
Operating conditions
2.3.1 In the case of citric, lactic and acetic acid separation:
— a column containing a strong cation (H+) exchange resin (300 mm length, 7.8 mm internal diameter, 9 m particle size) (e.g. HPX-87 H BIO-RAD),
— mobile phase: sulfuric acid solution, 0.0125 mol/L,
— flow rate: 0.6 mL/min,
— temperature: 60 - 65°C. (Depending on the type of resin).
2.3.2 In the case of fumaric, succinic, shikimic, lactic, malic and tartaric acid separation. — two columns (250 mm length, 4 mm internal diameter) placed in series,
fitted with octyl-bonded silica, spherical particles of 5 μm diameter, —mobile phase: potassium di-hydrogen phosphate solution, 70 g/L, ammonium sulfate, 14 g/L, and adjusted to pH 2.1 by adding phosphoric
acid, — flow rate: 0.8 mL/min, — temperature: 20°C.

## Slide 4
Method OIV-MA-AS315-18 Type II method Analysis of biogenic amines in musts and wines using HPLC
1. SCOPE
This method can be applied for analysing biogenic amines in musts and wines: Ethanolamine: up to 20 mg/l Histamine: up to 15 mg/l Methylamine: up to 10 mg/l
Serotonin: up to 20 mg/l Ethylamine: up to 20 mg/l Tyramine: up to 20 mg/l Isopropylamine: up to 20 mg/l Propylamine: normally absent Isobutylamine: up to 15 mg/l Butylamine: up to 10 mg/l Tryptamine: up to 20 mg/l Phenylethylamine: up to 20 mg/l Putrescine or 1,4-diaminobutane: up to 40 mg/l 2-Methylbutylamine: up to 20 mg/l 3-Methylbutylamine: up to 20 mg/l
Cadaverine or 1,5-diaminopentane: up to 20 mg/l Hexylamine: up to 10 mg/l

## Slide 5
6.3 Derivatisation
In a borosilicic glass tune (5.37), pour 2 ml of OPA solution (4.28), 2 ml of borate buffer (4.29), 0,6 ml of 2-mercaptoethanol (4.33). Close, mix (5.30). Open and pour 0,4 ml of sample. Close, mix (5.30). Inject immediately, as the derivitive is not stable. Rinse recipient immediately after injection, due to odour. Note: Derivatisation can be carried out by an automatic changer-preparer. In this case, the process will be programmed to come close to the proportion of manual derivisation
3. PRINCIPLE
The biogenic amines are directly determined by HPLC using a C18 column after O- phthalaldehyde (OPA) derivatization and fluorimetric detection.
TAG-FLUORESCENTE

## Slide 6
Method OIV-MA-F1-03 Sucrose by High-Performance Liquid Chromatography (Oeno 419A-2011)
4. Procedure
4.1 Preparation of sample: Use the solution obtained by diluting the rectified concentrated must to 40 % (m/v) as described in Annex H 'Total acidity', section 5.1., and filtering it using a 0.45 μm membrane filter.
4.2 Chromatographic determination Inject in turn into the chromatograph 10 μl of the standard solution and 10 μl of the sample prepared as described in 4.1. Repeat these injections in the same order. Record the chromatogram. The retention time of the sucrose is approximately 10 minutes. The sample volume and sequence are given for guidance. The chromatographic determination can also be done with a calibration curve
1. Principle
For testing and determination by high-performance liquid chromatography: the sucrose is separated in a column of alkylamine-bonded silica and detected by refractometry. The result is quantified by reference to an external standard analysed under the same conditions.

## Slide 7
Method OIV-MA-AS315-10 Measuring ochratoxine A in wine after going through an immunoaffinity column and HLPC with fluorescence detection (Oeno 16/2001 revised by Oeno 349-2011)
1. FIELD OF APPLICATION
This document describes the method used for determining ochratoxine A (OTA) in red, rosé, and white wines, including special wines, in concentrations ranging up 10 μg/l using an immunoaffinity column and high performance liquid chromatography (HPLC) [1].
2. PRINCIPLE
Wine samples are diluted with a solution containing polyethylene glycol and sodium hydrogen carbonate. This solution is filtered and purified on the immunoaffinity column.
OTA is eluted with methanol and quantified by HPLC in inverse state with fluorimetric detection.
5.3 HPLC analysis
Using the injection loop, inject 100 μl of reconstituted extract (equivalent to 2 ml of wine) in the chromatography.
Fluorescence detector:
Excitation wavelength = 333 nm
Emitting wavelength = 460 nm

## Slide 8
HPLC-Determination of nine major anthocyanins in red and rosé wine (Resolution Oeno 22/2003 modified by Oeno 12/2007)
1. FIELD OF APPLICATION
The analytical method concerns the determination of the relative composition of anthocyanins in red and rosé wine. The separation is performed by HPLC with reverse phase column and UV-VIS detection.
2. PRINCIPLE
Separation of the five most important non acylated anthocyanins (see Figure 1, peaks 1-5) and four major acylated anthocyanins (see Figure 1, peaks 6-9). Analysis of red and rosé wine by direct separation by HPLC by using reverse phase column with gradient elution by water/formic acid/acetonitrile with detection at 518 nm [1.2].
2.1 COLUMN
LiChrospher 100 RP 18 (5 μm) in LiChroCart 250-4 guard column: for example RP 18 (30-40 mm) in a cartridge 2 mm in diameter x 20 mm long
5.1 Preparation of samples
Clear wines are poured directly without any preparation into the sample vials of the automatic sample changer. Cloudy samples are filtered using a 0.45 μm membrane filter for HPLC sample preparation. The first part of the filtrate should be rejected.

## Slide 10
Méthode OIV-MA-AS315-27 Méthode Type IV Analysis of volatile compounds in wines by gas chromatography
(Resolution OIV-OENO 553/2016)
This method is applicable to the analysis of volatile compounds in wines containing less than 20 g/L sugar. For wines with a sugar content higher than 20 g/L and for mistelles, prior distillation (identical to that practised to obtain the ABV) is necessary; however distillation sometimes removes a significant part of the compounds.
2 – Scope of application
The present method may be used for the quantification of the following compounds (non-exhaustive list):
- ethanal,
- ethyl acetate,
- methanol,
- butan-2-ol,
- propan-1-ol,
- 2-methylpropan-1-ol,
- isoamyl acetate,
furfuraldehyde,
- (2R,3R)-butane-2,3-diol,
- (2R,3S)-butane-2,3-diol,
- butan-1-ol,
- 2-methylbutan-1-ol,
- 3-methylbutan-1-ol,
- pentan-1-ol,
- acetoin,
- ethyl lactate,
- hexan-1-ol,
- 3-ethoxypropanol,
- ethyl octanoate,
- propane-1,2-diol,
- butyrolactone,
- diethyl succinate,

## Slide 11
3 – Principle
Volatile compounds are quantified by gas chromatography after direct injection of the sample, added with an internal standard, into a capillary column coated with a bonded polar phase and detection using flame ionisation.
7 – Procedure
Analyse using the gas chromatograph with a capillary column
Analytical conditions (given by way of example):
Carrier gas (4.4): helium = 90 kPa
Septum flow rate: 2.5 mL/min
Split flow rate: 40 mL/min
Split mode of injection
Volume injected: 1 μL
9.Temperature of the injector: 200 °C Detector: FID (flame ionisation)
Detector temperature at 250 °C
Flame: hydrogen (4.3) = 50 kPa and Pair (4.5) = 130 kPa
Temperature programming:
. temp. 1 = 32 °C at 2.5 °C/min, up to 80 °C - t1 = 0 min
. temp. 2 = 80 °C at 4 °C/min, up to 170 °C - t2 = 20 min
. temp. 3 = 170 °C at 10 °C/min, up to 220°C - t3 = 20 min

## Slide 12
Method OIV-MA-AS323-10 Method of determination of phthalates by gas chromatography / mass spectrometry in wines
1. SCOPE
This method applies to the detection and assay of phthalates in wines.
2. PRINCIPLE
The sample is extracted using isohexane. The extract is concentrated by evaporation. The concentrated extract is analysed by gas chromatography/mass spectrometry (GC/MS) with deuterated internal standards.