## Slide 1
«ICSI Procedure and advanced techniques
in medically-assisted procreation»
Second-Cycle Degree Course in “REPRODUCTIVE BIOTECHNOLOGIES”
Ilaria Listorti
Head of Villa MafaldaART lab
ilistorti@unite.it
A.Y. 2022 - 2023

## Slide 2
virtual educational
and
scientific activities
THEROICAL LESSON
HUMAN EMBRYO CULTURE: TIPS AND TRICKS
- QUALITY CONTROL INSIDE A.R.T. LABORATORY
MAIN TOPICS
- MEET THE EXPERT

## Slide 3
WHAT IS EMBRYO CULTURE MEDIA?
Embryo culture is a component of in vitro fertilization;
Embryos are cultured in an atrificial medium consinsting of glucose, pyruvate and other energy-providing components;
The addition of amino acids, nucleotides, vitamins, and cholesterol may also improve the performance of embryonic growth and development;
Substances like antioxidants, antibiotics, macromolecules, hormones and growth factors can be added;
Optimization of the culture media is essential by optimizing all other components of the culture system, including the environment and equipment.

## Slide 4
Culture media is artificial but supports key functions:
Sperm function (motility, capacitation, acrosome reaction..)
Cleavage stage
Genomic actication
Early differentation of cell types
WHY CULTURE MEDIA IS SO IMPORTANT?

## Slide 5
1957: calcio lattato
in soluzione salina
1968: calcio lattato e acido
piruvico in soluzione complessa
Whitten, W. K. (1957). Culture of tubal ova. Nature, 179:1081-1082.
Whitten, W.K., Biggers, J.D. (1968). Complete development of in vitro of the pre-implantations stages of the mouse in a simple chemically defined medium. J. Reprod. Fertil. 17:399-401.
HUMAN EMBRYO CULTURE

## Slide 6
1998: “sequential” embryo
culture system
2004: “single-step” embryo
culture system
Gardner DK. 1998 Changes in requirements and utilization of nutrients during mammalian preimplantation embryo development and their significance in embryo culture. Theriogenology 49:83-102
Reed ML, et al., 2010 Challenging traditional embryo culture techniques with a simplified, continuous single medium protocol. J. Clin. Embryol 13:33-41
HUMAN EMBRYO CULTURE

## Slide 7
Step 2: CLEAVAGE
Non essential aminoacids
Low glucose
EDTA
Pyruvate
Lactate
Step 3: BLATOCYST
Non essential aminoacids
Essential aminoacids
High glucose
Pyruvate
Lactate
Sequential Culture System: “back to nature”
Step 1
Non essential aminoacids
Essential aminoacids
Low glucose
EDTA
Pyruvate
Lactate
Single-Step Culture System: “let the embryo choose”
Embryo genome
activation
DAY 1
DAY 2
DAY 3
DAY 4
DAY 5
Step 1: HTF
Non essential aminoacids
glucose
EDTA
Pyruvate
Lactate
DAY 0
HUMAN EMBRYO CULTURE

## Slide 8
110 h P. I.
ICSI 0 h
64 h P. I.
40 h P. I.
16 h P. I.
Embryo genome
activation
4 equal size cells
grade A embryo
2 PN zygote
8 equal size cells compatting
grade A embryo
cleavage medium
blastocyst medium
monophasic medium
HUMAN EMBRYO CULTURE

## Slide 9
Sequential media |  | Single-step media | 
pros | cons | pros | cons
mimic the natural environment | uneconomic culture system | easy to use | EDTA at blast
nutrients replenishment | risk of loosing | economic | ammonium accumulation
oil refreshment | busy management | little burocracy | nutrients depletion
little to no EDTA at blast | culture milieu disruption | autocrine and paracrine factors accumulation | catabolism accumulation
No ammonium accumulation |  | risk of loosing | oil oxidation
 |  | pH fluctuation | pH fluctuation
HUMAN EMBRYO CULTURE

## Slide 10
CULTURE STRATEGY
HUMAN EMBRYO CULTURE
INDIVIDUAL EMBRYO CULTURE
In small volume of culture medium (10-20 ml drop)
- Human is a monovulatory specie
- A bad embryo can be detrimental to the others
- Real traceability of every single embryo during culture
In large volume of culture medium (500 ml well)
- Human is a monovulatory specie
- A bad embryo can be dettrimental to the others
With large volume, the osmolarity increase slowly
GROUP EMBRYO CULTURE
In small volume of culture medium (25-50 ml drop)
- In-vitro conditions are different from the in vivo ones
Positive influence of paracrine factors
- Faster management of the entire embryo culture
In large volume of culture medium (500-1000 ml well)
- In-vitro conditions are different from the in vivo ones
Positive influence of paracrine factors
Faster management of the entire embryo culture
- No need for medium replenishment

## Slide 11
CULTURE STRATEGY
HUMAN EMBRYO CULTURE
Small volume of culture medium
Large volume of culture medium

## Slide 12
Media and consumables
Media PH and Co2 concentration
Oil and osmolarity
OPTIMIZING EMBRYO CULTURE SYSTEM

## Slide 13
pH PROFOUNDLY IMPACTS OOCYTES AND EMBRYOS
Oocyte mitochondrial localization and development competence, oocyte metabolism (correlated to maturational and developmental status). Denuded oocytes cannot regulate pH.
Embryo metabolic actitvity, intracellular organization, and overall embryo development;
Rate of blastomere division;
Fragmentation rates;
Overall embryo morphology.
pH

## Slide 14
pH SET BY %CO2 + [HCO3-] BUT TARGET UNKNOW
Optimal pH0 for human embryos is not yet determined
pHi of human embryos is tipically around 7.1
To avoid acidification, the lower level is therefore usually set at 7.2
Studies have suggested poorer embryo development at pH0 of > 7.4
Most media are used at 7.3 ± 0.1
pH0 is a function of HCO3- in media
HCO3- concentration is set by the manufacturer
%CO2 can be manipulated in the lab to control pH0

## Slide 15
FACTORS IMPACTING Ph LEVELS
Lenght of equilibration period
Frequency of incubetor door openings
Type of CO2 sensors
Temperature changes within the incubators
Bacterial/ fungal contamination
Altitude
Humidity

## Slide 16
CONTROL OF OSMOLARITY IS CRITICAL

## Slide 17
OPTIMIZING SYSTEMS: OSMOLARITY
Optimal volume per embryo is not yet determined;
Some labs successfully use 2-5 µl per embryo, more tipically 20-50 µl;
Drop size may affect longer term changes in osmolarity;
More care needed during dish preparation, example...
One dish at a time;
Evaluate type of dish;
Airflow minimized;
Underlay drops;
Use maximum oil volume;
Evaluate type of oil

## Slide 18
LOW VS HIGH OXYGEN CONCENTRATIONS FOR EMBRYO CULTURE

## Slide 19
OPTIMIZING SYSTEMS: TEMPERATURE
Suggestion that temperatures below 37°C may give better outcomes
Temperature above 37°C NOT reccommended

## Slide 20
OPTIMIZING SYSTEMS: ROLES OF OIL
Oil have different roles in optimizing a culture systems:
Minimizes pH shift;
Prevents changes in osmolarity;
Reduces risk of temperature fluctuation;
Protects samples from contamination, paticularity VOCs from gas supply, plastic ware and general lab environment
Use maximum amount of oil in culture dish

## Slide 21
THEROICAL LESSON
HUMAN EMBRYO CULTURE: TIPS AND TRICKS
- QUALITY CONTROL INSIDE A.R.T. LABORATORY
MAIN TOPICS
TARGET: DON’T DO THAT

## Slide 22
PRESENCE OF
QUALITY CONTROL
ABSENCE OF
QUALITY CONTROL
BIOLOGICAL PROCESS
OUT OF CONTROL
LOW RESULTS
FLUCTUATING RESULTS
NO SECURITY
ECONOMIC IMBALANCE
FRUSTRATION
BIOLOGICAL PROCESS
UNDER CONTROL
HIGH RESULTS
REPEATABLE RESULTS
SECURITY
SAVE MONEY
HAPPINESS - SATISFACTION
TARGET: DO THAT

## Slide 23
LABORATORY FACTORS THAT CAN AFFECT OUTCOME OF IVF
Air quality;
Pipettes/hyaluronidase/denudation;
Warm surfaces/stages;
Microscope light;
Culture medium;
Culture dishes;
Protein supllementation;
Cuture oil;
Incubator gas/temperature;
Incubatore gas partial pressure.

## Slide 24
QUALITY CONTROL
“sperm survival test”: donor sperm survival
after 24-48 h of culture inside icubator
“VOC’s test”: inorganic volatile compounds
“LAL test”: endotoxins presence

## Slide 26
1. INCUBATORS
Temperature (it depends on plasticware):
36.5 – 37.5 °C
(check every day)
(calibrate every 2 months)
Gas flow (CO2 – O2 – N2):
15 – 25 kPA/min
(check 1 a year)
CO2/O2 (it depends on culture media)
5% - 6%
(check every day)
(calibrate every 2 months)
QUALITY CONTROL

## Slide 27
2. GAS PLANT
Temperature:
36.5 – 37.5 °C
Entering pressure:
max 1.5 bar
assenza perdite
entrata
assenza perdite
uscita
QUALITY CONTROL

## Slide 28
3. WORKSTATION
Temperature: 36.5 – 37.5 °C
(check every day)
(calibrate every 2 months)
Light intensity
Light beam condensation
(check every day)
Flow intensity (2 time a year)
Particles count (2 time a year)
Microbic count (2 time a year)
QUALITY CONTROL

## Slide 29
4. MICROMANIPOLATION STATION
integrity, accuracy,
precision of mincoinjection system
Temperature
(it depends on plasticware):
36.5 – 37.3 °C
(check every day)
(calibrate every 2 months)
Temperature
(it depends on plasticware):
36.5 – 37.3 °C
(check every day)
(calibrate every 2 months)
QUALITY CONTROL

## Slide 30
integrity, accuracy,
precision of mincoinjection system
QUALITY CONTROL

## Slide 31
ICSI 0 h
40 h P. I.
64 h P. I.
16 h P. I.
110 h P. I.
QUALITY CONTROL: DEVELOPMENT INDICATORS

## Slide 32: SUMMARY
To achieve optimal results in an IVF lab. Attention to detail, adherence to protocols and QC are vital!!!
IVF culture media is an integral part of the embryo culture system. Its use must be optimized in every laboratory;
pH, temperature and osmolarity must be carefully monitored and maintained;
Choice and use of oil is critical;
Consumables and equipment should be of the highest quality, tested regulary and maintained, where appropriate

## Slide 33
Meet the Expert
All about Intra Cytoplasmic Sperm Injection (ICSI)
https://www.youtube.com/watch?v=i4phDnDuSdY
Trophectoderm biopsy and tubing of cells for preimplantation genetic testing
– part 1
https://www.youtube.com/watch?v=FyBh_814jtI#action=share
– part 2
https://youtu.be/19JUcdISuAM